## Slide 1
Using Handcar Cosim APIs
IC Labs – CPU Group
Robert Chu
April 21, 2021
FUTUREWEI

## Slide 2
Where Does Handcar Cosim API DLL Fit-In?
FUTUREWEI
<number>

## Slide 3
Building the Handcar Cosim API DLL
git clone https://github.com/openhwgroup/force-riscv
export FORCE_CC=/usr/bin/g++
export FORCE_PYTHON_VER=3.6
export FORCE_PYTHON_LIB=/usr/lib/x86_64-linux-gnu/
export FORCE_PYTHON_INC=/usr/include/python3.6
cd force-riscv/handcar
./regenerate_and_build.bash
#library located in <force-riscv>/handcar/bin/handcar_cosim.so
#inc and src located in:
# <force-riscv>/handcar/so_build/cosim/inc/handcar_cosim_wrapper.h
# <force-riscv>/handcar/so_build/cosim/src/handcar_cosim_wrapper.cc
FUTUREWEI
3

## Slide 4
vcs Compile with Handcar Cosim API DLL
vcs … $FORCE_RISCV/handcar/bin/handcar_cosim.so …
FUTUREWEI
4

## Slide 5
UVM Import
import “DPI-C” function void initialize_simulator(input string options);
import “DPI-C” function int step_simulator(input int target_id, input int num_steps, input int stx_failed);
import “DPI-C” function int get_disassembly_for_target(input int target_id, input bit[63:0] pc, inout string opcode, inout string disassembly);
import “DPI-C” function int read_simulator_memory(input int target_id, input bit [63:0] addr, inout int length, output bit [63:0] data);
import “DPI-C” function int write_simulator_memory(input int target_id, input bit [63:0] addr, input in length, input bit [127:0] data);
import “DPI-C” function int read_simulator_register(input int target_id, input string reg_name, output bit [127:0] reg_data, input int length);
Import “DPI-C” function int write_simulator_register(input int target_id, input string reg_name, input bit [127:0] reg_data, input int length);
FUTUREWEI
5

## Slide 6
Usage Example – Initializing ISS
string init_opt_str;
…
init_opt_str = $sformatf(“-p%0d –hartids=“, num_proc);
…
for (i = NUM_CPUS-1; i >= 0; i--) begin
if (i > 0)
init_opt_str = $sformatf(“%s%0d,”, init_opt_str, CPU_IDS[i]);
else
init_opt_str = $sformatf(“%s%d”, init_opt_str, CPU_IDS[i]);
end
initialize_simulator(init_opt_str)
FUTUREWEI
<number>

## Slide 7
Usage Example – Initializing ISS Memory
while (! $feof(hex_file_fd))
begin
code = $fscanf(hex_file_fd, “%h %h”, addr, data);
if (code != -1)
begin
ret_status = write_simulator_memory(target_id, addr, length, data);
if (ret_status !=0)
begin
uvm_error(“ISS ERROR”,
$sformatf(“Cannot write ISS memory for cpu=%0d at addr=0x%h”,
target_id, addr));
end
end
end
FUTUREWEI
<number>

## Slide 8
Usage Example – Step and Compare
// track rtl commit/retire in monitors (in rtl_txn, or a queue of rtl txns)
ret_status = read_simulator_register(target_id, “PC”, iss_txn.pc, pc_length);
if (ret_status != 0)
begin
uvm_error(“ISS ERROR”,
$sformatf(“Couldn’t obtain ISS PC value for cpu=%0d”, target_id));
end
if (rtl_txn.pc != iss_txn.pc)
begin
uvm_error(“MISMATCH”,
$sformatf(“cpu=%0d has rtl PC (0x%h) mismatch ISS PC (0x%h)”,
target_id, rtl_txn.pc, iss_txn.pc));
end
// advance the PC
ret_status = step_simulator(target_id, step_num, /*stxr_status*/0);
if (ret_status != 0)
begin
uvm_error(“ISS ERROR”,
$sformatf(“ERROR: ISS can’t move forward for cpu=%0d, step_num=%0d”,
target_id, step_num));
end
FUTUREWEI
<number>