## Slide 1: Hardware Abstraction Layer (HAL) Requirements
Prepared for SW TG
June 2021

## Slide 2: Version
Version | Date | Contributors
1 | May 31 /2021 | Duncan Bees - initiation
2 | June 7/2021 | Added comments from Jeremy Bennett
3 | June 9/2021 | Added comments from Yunhai Shang
4 | June 19/2021 | Updated following SW TG meeting of June 14 to add diagram

## Slide 3: Purpose
To agree high-level requirements driving selection of HAL technical approach

## Slide 4: What is the HAL
A software API framework on CORE-V based processors
Provides unified, consistent access for the operating system layer to
  on-core hardware functions
  on-chip, outside the core hardware functions
  excluded for now: on-board, outside the chip hardware functions
Provides a well accepted framework for driver-layer API (access to peripherals) and core-layer API (access to the core) that can be extended as CORE-V family grows
Provides a standard to describe the resources in the chip
Allows developers to generate a configuration file for use by higher layer software (see requirements)

## Slide 5: Diagram (to be checked)
BSP
CORE-V CORE
HAL Interface
RTOS/bare-metal
Application
Application
Application
HW
SW
on-chip peripherals
Compare to FreeRTOS HAL diagram
http://freertoshal.github.io/doxygen/group__HAL.html
HAL

## Slide 6: HAL Technical Features
HAL MUST support API for core features
HAL MUST support API for on-chip peripheral features
HAL MUST support both RTOS and bare-metal scenarios
HAL MUST be able to support bare metal libc
HAL MUST be able to be extended to support all CORE-V cores for the purpose of RTOS (not Linux) support
HAL MUST support a description of the chip using a standardized syntax
HAL SHOULD define a configuration file that can indicate to the IDE low level chip parameters such as memory space and allow it to display/read/write the registers of peripherals

## Slide 7: Technical Features For further study
HAL MAY be able to be extended to support the CORE-V X Coprocessor Interface (CV-X-IF)
HAL MAY be able to be extended to support the CV-VEC coprocessor

## Slide 8: HAL – Industry Adoption Requirements
HAL SHOULD be adopted/implemented for other RISC-V devices

## Slide 9: HAL Specification for CORE-V
HAL Specification License for CORE-V MUST be open-source or freely licensed
Proprietary extensions to the HAL Specification and Implementation, such as for custom ISA extensions or proprietary chip, MUST be supportable/allowable under open-source license
HAL Specification, user documentation, and system implementation documentation for CORE-V HAL MUST be available in English
HAL Specification MUST be published and managed by an industry open source or standards body, such as OpenHW, RISC-V International, or FOSSi

## Slide 10: HAL Implementation for CORE-V
A complete open source reference implementation of the HAL for CORE-V MUST be a project deliverable
FreeRTOS SHOULD be supported in the open source reference implementation of HAL for CORE-V
Newlib SHOULD be supported in the open source reference implementation of HAL for CORE-V
The HAL reference implementation for CORE-V SHOULD be published by the body publishing the Specification (previous page)

## Slide 11: Suggested Next Steps
SW TG edit the requirements presentation to consensus
Agreed requirements form part of HAL Project Concept to be reviewed in special meeting June 21
TWG June 28 reviews Project Concept June 28
Agreed requirements drive selection of HAL approach to be reviewed in SW TG July 12
HAL Project Launch reviewed in TWG July 26