## Slide 1: CV32E20 Project Concept (PC)
Proposed CV32E20 Project Concept
  Co-sponsored by NXP and Intrinsix
Ultra-low-end core based on ETH-Zurich ZeroRISCY
  Use the IBEX core RTL design as the starting point
    Intended as “minimum size” 32-bit RISC-V processor
    Support for “micro” and “small” configurations
  Optimized for minimum gate count and lowest power
  Qualified using industry-strength verification and architecture compliance techniques
Targeted at the low-end of RISC-V MCU roadmaps
  Any “compute constrained socket”
  Processor element in embedded SoC subsystems
https://github.com/lowRISC/ibex/blob/master/README.md

## Slide 2: CV32E20 Project Concept (PC) Continued
Consideration for a multi-phase development
  Phase 1: RTL design of Core starting from Ibex
    RV32IMC and RV32EMC
    OBI bus interface
    CV32E40P like interrupt interface
    User and Machine privilege mode
  Phase 2: Create core-complex
    OBI to AHB-5 bridges (Intrinsix base)
    Interrupt controller design INTC (OpenTitan of Pulp base)
    Debug design (Pulp of implementation of ratified debug spec)
Future Design Enhancements
    Support for new compressed opcodes (Zce)
    Exploration of 2-pin CJTAG debug interface
    Exploration of ETH-Zurich’s “Tiny FPU”
    Low granularity Physical Memory Protection module (PMP)
Project resourcing
  NXP contributes architecture resource
    Joe Circello (joe.circello@nxp.com)
  Intrinsix contributes verification resources
    Lee Hoff (lhoff@intrinsix.com)
https://github.com/lowRISC/ibex/blob/master/README.md