## Slide 1
CV32E40P v2 Project Concept
Olivier Monfort, Pascal Gouedo
Dolphin Design
June 28, 2021

## Slide 2
Dolphin Design

## Slide 3
Target of CV32E40P v2 is integration in
  PANTHER multicore cluster
Final PANTHER delivery packaging is
  2022 Q2
CV32E40P v2 use case for Dolphin Design

## Slide 4
High Level Summary of project
Verifying XPULP, RVF, and Zfinx ISA extensions that were disabled during CV32E40P v1 phase improving performances, power consumption and code size depending of application programs
Who would make use of OpenHW output
Companies needing more performances, less energy consumption or smaller code size for
  Standard control applications
  DSP-like computing applications
Explanation of why OpenHW should do this project
Finalize CV32E40 as originally intended in the CV32E40 Features and Parameters to propose a more powerful/optimized version of CV32E40
Project Concept

## Slide 5
Re-Encode in Custom extension and Verify PULP “basic” instructions which
  Improve performances and power consumption
  And even reduce code size depending of application programs
  They are
    Post-increment and register-register indexed load/store
    Hardware Loops
    General ALU extensions
    Immediate Branch
    Multiply and Accumulate
Re-Encode in Custom extension and Verify Bit Manipulation and SIMD PULP instructions which
  Improve performances and power consumption on specific workloads
Project Requirements

## Slide 6
Re-Encode in Custom extension and Verify PULP instructions used for Cores synchronization
  PULP Event load
For Multicore cluster area reduction,
  Verify PULP Zfinx?
  or Re-Design (if needed) and Verify Zfinx as described in zfinx-spec-20210511-0.41?
  Make it optional with a parameter?
Floating Point Unit
  Keep FPU instructions decoding inside the Core and dispatch to APU interface and Verify RISC-V standard F extension instructions (Zfinx and non-Zfinx) with coupled Core-FPnew?
  or Merge ETH CV-X-IF and only Verify this interface?
Project Requirements

## Slide 7
Conversion of PULP Bit Manipulation & SIMD instruction to ratified RISC-V B and P extensions.
Add Zce extension for further code-size reduction (not required for Multicore cluster).
Add bus attributes and errors.
Potential future design enhancements

## Slide 8
Initial Estimate of Timeline
Preliminary RTL release in 2021 Q4
Implementation of the test plan is assumed to be started in July/August 2021
Verification is expected to complete in 2022 Q1
Industry landscape: description of competing, alternative, or related efforts in the industry
ARM Cortex M4
Project Concept

## Slide 9
OpenHW Members/Participants committed to participate
Dolphin Design - Design & Verification
Technical Project Leader(s)
At of Project Concept, led by Pascal Gouedo, Dolphin Design
Project Concept

## Slide 10
Next steps/Investigation towards Project Launch
Verification to be assessed in detail
  Google ISG
  Imperas reference model
  SW GCC toolchain support
Confirmation of Resources & Schedule
Additional information
OneSpin RISC-V and FPU apps as well as 360 DV-Verify licenses purchased by Dolphin Design for this Multicore cluster industrialization
Project Concept