## Slide 1: Verification TG – E* Core Status September 16, 2021
Steve Richmond steve.richmond@silabs.com

## Slide 2: Outline
Administration
CV32E40X
  Active Tasks
  Next Tasks
  Formal
CV32E40S
  Next Tasks
Open Issues

## Slide 3: Administration
This will be a monthly meeting on general E-core status and project coordination
Reminder that attendance will be taken at all meetings
  Attendance ensures voting eligibility per OpenHW bylaws

## Slide 4: General Updates
CV32E40X
  Reworked pipeline nearly fully passing random simulations
    Scope: Legacy (cv32e40p) random simulations
    RVFI debug/interrupt corner case condition
  Bus errors implemented in RTL
    Directed OBI-I testcases running
    Random OBI-I testcases in debug
    Directed OBI-D TBD
  B extension implemented
    Directed test running

## Slide 5: CV32E40X – Active Tasks
Project task board updated:
  https://github.com/openhwgroup/core-v-verif/projects/11
Refresh interrupt vplan (678)
  Interrupt vplan in cv32e40x needs updates for:
    New instruction extensions inline with external interrupt and WFI events
    Ensuring the RVFI interrupt is signaled with respect to the microarchitecture (i.e. the properties)
Remove irq_ack_o from testbench infrastructure (705)
  Cores team is removing irq_ack_o (h/w ack interface for interrupts)
  Will maintain internal signal to keep testbenches portable

## Slide 6: CV32E40X – Active Tasks
Implement random instruction bus errors (872)
  Injecting random OBI-I errors – done
  Ensure that programs can progress to completion
    Order of OBI bus errors can make “recovery” impossible
    core-v-verif needs updated to ensure the bootstrap pins make exception vectors available from first instruction (preferably random)
    Need to test OBI-I errors in all scenarios (initial fetch, in exceptions, debug, normal execution, etc)

## Slide 7: CV32E40X – Active Tasks
Implement PMA random testing (873)
  core-v-verif implements address maps via linker scripts
  riscv-dv can only randomize via “data pages”
  Implementing a linker generator and extensions in corev-dv to enable automated address/region generation via linker scripts
  Highlights weakness of core-v-verif with respect to parameter (variant) regression and testing
    Need to be able to cross tests and configurations in test building, results collection, simulation and regression
  Will highlight/review solution at next VTG

## Slide 8: CV32E40X – Next Tasks
Port compliance test to architecture test framework (530)
Refresh debug plan (679)
  Add external debug request to rvfi_dbg verification
Create fence.i vplan (871)
  Includes requirements of UVM agent and microarchitecture checking and coverage
Create vplan for Zce (870)
Next…
  OBI-D bus errors (directed and random) and NMIs
  Fence.i implementation

## Slide 9: CV32E40X - Formal
OpenHW staff currently bringing up OneSpin RISCV formal tool on CV32E40P
  Runs on OpenHW cloud
Plan to bring this to the CV32E40X next

## Slide 10: CV32E40S – Next Tasks
Stand up cv32e40s/dev and cv32e40s/release (874)
  User mode should be implemented enough in RTL to pass ci_check

## Slide 11: Open Issues?